## Slide 1: Plateforme de l’ICMMO
Service Magnétométrie

## Slide 2: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
MPMS 5 (1996) :
  dc measurements,
  2-400K, (temperature sweep mode from 5 to 400K
  +/- 5T

## Slide 3: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
XL7 (2012) :
  2-400K, up to 7T, dc measurement,
  RSO,
  ac measurement (0.1-1500Hz),
  oven option: up to 800K (SP2M team)
  He reliquifier (Cryomech PT410)

## Slide 4: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Photomagnetic measurements:
UV/Vis or Vis/IR Fiberoptic Sample Holder

## Slide 5: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Lightning sources:
Pulsed Laser Surelite Continuum
355nm +
OPO (410-1600 nm)
20 mW/cm² on the sample
Source l = 355 nm
Cristal de BBO
(b BaB2O4)
Fiber coupling
« Idler » l > 710 nm
« Signal » 400< l < 710 nm
Source
l = 355 nm

## Slide 6: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Continuous Wave Sources:
Laser Diode (100mW max) : 405, 473, 532, 635 nm
Low-power diode (5 mW) 1290-1330 nm
LED (50 mW max) : 365, 375, 385, 505, 590, 850 nm

## Slide 7: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
Molecular Complexes
Complexes moléculairesTrinuclear Manganese Complexes of Unsymmetrical Polypodal Diamino N3O3 Ligands with an Unusual [Mn3(μ-OR)4]5+ Triangular
Core: Synthesis, Characterization, and Catalase Activity, Inorg. Chem. 2014, 53, 2545−2553
(a) Temperature dependence of χMT for compound 1ClO4: (O) experimental data, solid line in red shows the simulation obtained with the isotropic Hamiltonian (fitting in the range 300−50 K), solid line in blue corresponds to the best fit including a local zero-field splitting parameter D (fitting in the range 300−2 K). (b) Magnetization vs H/T curves recorded at 2, 4, 6, and 10 K. Solid lines correspond to the curves determined using the parameters deduced from the χMT = f(T) curve.

## Slide 8: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
Single Molecule Magnet
Structural and Electronic Dependence of the Single-Molecule-Magnet Behavior of Dysprosium(III) Complexes, Inorg. Chem. 2014, 53, 2598−2605
Perspective showing the distorted bicapped square-antiprismatic geometries of the central dysprosium(III) ion for 1 (a and b) and 2 (c and d).
ac susceptibility data for complexes 1 (a and b) and 2 (c and d). Plots of χ′ (a and c) and χ″ (b and d) versus temperature at different wave frequencies under a dc field (H = 1000 Oe).
Cole−Cole plots obtained for complexes 1 (a) and 2 (b). The solid lines represent the fit obtained with a generalized Debye model.

## Slide 9: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
Nanoparticules
Magnetization Reversal in CsNiIICrIII(CN)6 Coordination Nanoparticles: Unravelling Surface Anisotropy and Dipolar Interaction Effects, Adv. Funct. Mater. 2014, 24, 5402–5411
TEM images of the nanoparticles [8], [10], [12], [16], [18] and [22] embedded in DODA+ (top, scale bar: 100 nm) and HRTEM images of the nanoparticles [6] (bottom left, scale bar: 5 nm) and [30] (bottom right, insert: electronic diffraction pattern).
Out-of-phase component, χ″, of the magnetic susceptibility at 1 Hz for the highly diluted samples [6_dil] (●), [8_dil] (◻), [10_dil] (▴), [12_dil] (⋄), [16_dil] (▾), [18_dil] (+) and [22_dil] (×).

## Slide 10: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
Spin Convertion / LIESST effect
Light-induced excited spin state trapping effect on [Fe(mepy)3tren](PF6)2 solvated crystals. Dalton Trans., 2014, 43, 1063–1071
Molecular structure of the [Fe(mepy)3tren]2+ cation at 10 K
Magnetic measurement of the Fe(mepy)3tren](PF6)2·C7H8·C2H3N sample performed with a sweeping rate at 0.3 K min−1: on cooling (blue), upon irradiation at 10 K with λ = 532 nm (black) and upon heating in the dark after reaching the photostationary state at 10 K.
HS-to-LS relaxation curves performed with magnetization measurements at different temperatures (○), along with their modelization in the mean-field approximation (-).

## Slide 11: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
LIESST Effect (2)
Photomagnetic effect in a cyanide-bridged mixed-valence {FeII2FeIII2} molecular square, Chem. Commun., 2012, 48, 5653–5655
View of the cyanide-bridged {FeIII2FeII2} square unit with the atom labelling for the metal environments. The hydrogen atoms are omitted for clarity. C: gray, N: blue, O: red, B: pale blue, FeIII: yellow, FeII: orange
Magnetization vs. irradiation time of a dehydrated sample of 1 at different Wavelengths (7 mW/cm2).

## Slide 12: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
Molecular-scale devices
Tailor-made Nanometer-scale Patterns of Photo-switchable Prussian Blue Analogues, Adv. Mater. 2010, 22, 3992–3996
Temperature dependence of the magnetization under an applied field of 30 000 Oe of B) the PBA-free nanoperforated titanium oxide film coated on a gold layer and D) the nanocomposite coated on a gold layer before irradiation (white square) and after irradiation (black circle). A NiO antiferromagnetic thin pellet was added to the films in order to optimize the signal to noise ratio.
CoFe PBAs of chemical formula CxCo4[Fe(CN)6](8 + x)/3·H2O (C is an alkali cation) is well tuned, they are composed of CoIII(low spin, LS) and FeII(LS) diamagnetic ions at low temperature. Irradiation in the visible range induces the CoIII(LS)FeII(LS) → CoII(high spin, HS)FeIII(LS) electron transfer.

## Slide 13: Plateforme Instrumentale de l’ICMMO Service Magnétométrie Université Paris-Sud
Area of competence :
Measurement of molecular networks on surfaces
Cyanide-bridged NiCr and alternate NiFe–NiCr magnetic ultrathin films on functionalized Si(100) surface, Dalton Trans., 2012, 41, 4445–4450
Growth of NiCr films on Ni0 anchoring sites. SGS were performed on the Ni0 anchoring sites that form a relatively flat monolayer on a Si(100) substrate. We carried out SGS by immersing alternatively the functionalized substrate in an aqueous solution of [Cr(CN)6]3− (steps Cr1, Cr2,…Crn) and in a methanolic solution of Ni(H2O)6 2+
NiCr SGS (6 cycles): a) Evolution of the intensity of the infrared asymmetric vibration band of cyanide at each step from the step Ni1 to Ni6 and corresponding peak area. b) AFM image and size distributions of the objects at the step Ni6. c) M = f(T) curves at H = 100 Oe for a bare silicon wafer (left) and at the step Ni6 of NiCr SGS (right) – plain circles: ZFC, open circles: FC.
Notes: Interaction ferro entre le Ni et les Cr, et surement interaction ferro entre les plots (taille des plots de 3nm => Tb < 5K ici Tb = 8K)